# Enstore Installation
## Introduction
Enstore is written in python and currently requires a slightly modified python language interpreter. Enstore uses a Fermi Tape Tool (FTT) library and set of tools providing access to different types of tape drives. It is included into enstore rpm for the revisions later than 2.0.0-0. This section describes installation and configuration procedures of enstore and all required additional software.

### Remote access
Before installing enstore you need to set up all its nodes for remote access.
Remote access and product distribution is provided by the following scripts in $ENSTORE_DIR/sbin coming with enstore rpm:
1. enrsh - analog of rsh
2. enrcp - analog of rcp
3. enrsync - analog of rsync

2 options are currently provided for secured access: kerberized rsh and rcp, and ssh.
For using either of them you need to setup kerberized or (and) ssh access to all enstore nodes for 'enstore' and 'root' accounts.
The mentioned scripts first check for the presence of the directory containing kerberized utilities. If it is found they assume that krb5 utilities will be used. If $ENSSH or $ENSCP are defined the ssh and scp will be used. As the last resort they try to use non kerberized rsh, rcp, and rsync. Installation and configuration of ssh and kerberized rsh, rcp are out of the scope of this document.

### Enstore rpm

The enstore rpm and additional rpms are located here ftp://ssasrv1.fnal.gov/en/. Currently there are rpms for SL4, SL5, and SL6. They are located in lts44, slf5x, and slf6x sub directories correspondingly.
For other OS versions please check enstore download page or contact enstore mailing list. It is desirable that X-windows is installed at least on head node. This allows to run entv – application which dynamically shows data transfers.
Installation of enstore always begins on enstore head node - the node where configuration server will be running.
### Installing Enstore.
If you install the new enstore instance (site) the installation must begin on enstore head node – the node, where enstore configuration server will run.
Enstore has 2 kinds of configurations – servers and movers. Mover require less products installed (minimal installation), but may be installed as Enstore server.

#### Minimal installation (mover node)
Install the following rpms:mt-st, posgresql-libs, enstore. Example:
[root@enmvr026 ~]# yum -y install mt-st
[root@enmvr026 ~]# rpm -ivh ftp://ssasrv1/en/slf5x/x86_64/postgresql-libs-8.4.3-1PGDG.rhel5.x86_64.rpm
[root@enmvr026 ~]# rpm -Uvh ftp://ssasrv1/en/slf5x/x86_64/enstore-3.3.0-0.x86_64.rpm

#### Complete installation (server node)
For complete installation in addition to the minimal installation install postgresql server (can be done different ways) and the following rpms: tcl, tk, httpd, ncompress, gnuplot, ImageMagick. Example:
[root@enmvr026 ~]# yum -y install tcl tk httpd ncompress gnuplot ImageMagick
[root@enmvr026 ~]# rpm --force -ivh ftp://ssasrv1/en/slf5x/x86_64/postgresql*
--force was used to ignore installed postgresql-libs
[root@enmvr026 ~]# rpm -ih ftp://ssasrv1/en/slf5x/x86_64/compat-postgresql-libs-4-1PGDG.rhel5.x86_64.rpm

### Configuring Enstore

Enstore configuration includes run-time environment, enstore site (instance) configuration – enstore configuration file, and distributed environment configuration. When enstore rpm is installed the user account “enstore” is created and its .bash_profile and .bashrc are modified. The changes are done to the system allowing to start enstore on boot (/etc/rc.d/init.d/enstore-boot, /etc/rc.d/init.d/monitor_server-boot).

#### Run-time environment.

Enstore run-time environment can be initially created on Enstore head node and then copied all nodes running enstore servers and movers – all nodes where enstore was installed and will be using this particular enstore instance (site).
##### Head node
Assuming that we are configuring the head node, login to head node as user “enstore”. Do the following:
[enstore@enmvr026 ~]$ whoami
enstore
[enstore@enmvr026 ~]$ pwd
/home/enstore
[enstore@enmvr026 ~]$ mkdir -p site_specific/config
[enstore@enmvr026 ~]$ cp /opt/enstore/site_specific/config/setup-enstore site_specific/config
Modify the following lines in site_specific/config/setup-enstore:
export ENSTORE_CONFIG_HOST= # put here the name of your head node
export ENSTORE_CONFIG_FILE= # put here the path for enstore configuration file
export ENSTORE_MAIL= # put here email address for system administrators
For particular FNAL enstore instances see this.
For more details on enstore configuration file see /opt/enstore/enstore-installation.pdf

##### Regular node
If enstore instance has multiple nodes copy enstore configuration from head node to these nodes:
[enstore@new_node ~]$ pwd
/home/enstore
[enstore@new_node ~]$ mkdir -p site_specific/config
[enstore@new_node ~]$ scp gccenmvr16a:site_specific/config/* site_specific/config

#### Farmlets
Farmlets are the files containing node names for distributed operations on enstore nodes. These files are used by rgang command (multinode analog of rsh). You need to create initial farmlets and then add and modify them when adding or removing an enstore node.
Initially farmlets can be created by /opt/enstore/external_distr/make_farmlets.sh script or manually. You have to create enstore configuration file before running make_farmlets.sh. More details can be found in /opt/enstore/enstore-installation.pdf.

#### Name Space
Enstore client (encp) uses name space to present files to users. The files are arranged into directories and can be viewed using Unix FS commands such as “ls”, “pwd”. This name space was initially provided by pnfs, replaced later by chimera. Chimera is part of dcache project which means that to have chimera dcache rpm needs to get installed form dcache web site. Below is the example of dcache installation and configuration to run chimera name space. Note that the name space service need to get installed only on the node where it will be running. This service can be installed on every server in the framework of Screw Driverless Enstore (SDE) project, which requires the similar installation on all Enstore servers to provide easy replacement of the Enstore services in case of failure. Dcache is implemented in java, so install java (for instance):
[root@gccenmvr16a]# rpm -ivh http://javadl.sun.com/webapps/download/AutoDL?BundleId=78696
Install dcache rpm:
[root@gccenmvr16a]# rpm -ih http://www.dcache.org/downloads/1.9/repo/2.2/dcache-2.2.15-1.noarch.rp
Configure dcache to run name server on gccenmvr16a
root@gccenmvr16a]# cd /etc/dcache/
[root@gccenmvr16a]# cp -p dcache.conf dcache.conf.orig
Modify dcache.conf:
dcache.layout=${host.name}
dcache.namespace=chimera

chimera.db.user=enstore
chimera.db.url=jdbc:postgresql://localhost/chimera?prepareThreshold=3

defaultPnfsServer=gccenmvr16a.fnal.gov
hsmStorageInfoExtractor=org.dcache.chimera.namespace.ChimeraEnstoreStorageInfoExtractor
dcache.log.mode=new
scripts=${dcache.home}/scripts
scheme=development
dcache.user=root
Create layout:
[root@gccenmvr16a dcache]# cd layouts/
Create gccenmvr16a.conf:
[dCacheDomain]
[dCacheDomain/poolmanager]
[dCacheDomain/broadcast]
[dCacheDomain/loginbroker]
[dCacheDomain/topo]

[namespaceDomain]
dcache.java.memory.heap=2048m
dcache.java.memory.direct=2048m
[namespaceDomain/pnfsmanager]
pnfsVerifyAllLookups=true
[namespaceDomain/cleaner]

[nfsDomain]
dcache.java.memory.heap=2048m
dcache.java.memory.direct=2048m
[nfsDomain/nfsv41]
cell.name=NFS-${host.name}
nfs.v3=true
nfs.domain=fnal.gov
nfs.idmap.legacy=true

[dirDomain]
[dirDomain/dir]

Create DB directory (this must be on a separate large disk – external RAID):
as “root”
[root@gccenmvr16a]# mkdir /chimera
[root@gccenmvr16a]# chown enstore.enstore /chimera
as “enstore”
[enstore@gccenmvr16a ~]$ /usr/pgsql-9.2/bin/initdb -D /chimera

as “root”
[root@gccenmvr16a]# service postgresql-9.2 start
Starting postgresql-9.2 service: [ OK ]
[root@gccenmvr16a]# createdb -U enstore chimera
Add line to /etc/fstab:
localhost:/ /pnfs/fs nfs sync,rsize=4096,wsize=4096,user,intr,bg,hard,rw,noac,vers=3,nolock 0 0
Add lines to /etc/export (it must be later extended with names of client machines):
[root@gccenmvr16a]# echo "/ localhost(rw,no_root_squash)" >> /etc/exports
[root@gccenmvr16a]# echo "/pnfs/fs localhost(rw,no_root_squash)" >> /etc/exports
Create /pnfs/fs:
[root@gccenmvr16a]# mkdir -p /pnfs/fs
Start chimera server
[root@gccenmvr16a pgsql]# chkconfig --add dcache-server
[root@gccenmvr16a pgsql]# chkconfig dcache-server on
[root@gccenmvr16a pgsql]# service dcache-server start
Mount /pnfs/fs:
[root@gccenmvr16a]# mount /pnfs/fs
Check that chimera works:
[root@gccenmvr16a pgsql]# mkdir -p /pnfs/fs/usr/demo_test
[root@gccenmvr16a pgsql]# touch /pnfs/fs/usr/demo_test/aaa
[root@gccenmvr16a pgsql]# ls /pnfs/fs/usr/demo_test
aaa

### Finishing installation and configuration
After enstore was installed and configured start enstore configuration server. This is needed to install and configure:
- enstore web site
- enstore cron jobs
- enstore databases
  To start enstore configuration server login to enstore head node as user “enstore” and do the following:
  [enstore@enmvr026 ~]$ enstore start --just config
Checking configuration_server.
Starting configuration_server
[enstore@enmvr026 ~]$ enstore conf –show
This command will output the enstore configuration described in $ENSTORE_CONFIG_FILE.
Note!!! All enstore commands have –help option. If you do not know what can be done just type enstore and investigate what options are available. Also refer to “Enstore Admin Guide” (can be found in /opt/enstore/doc/guides/Enstore_Administrator_Guide.pdf)
#### Enstore web site
After enstore was installed and configuration server started install enstore web site:
[root@gccenmvr16a ]# /opt/enstore/sbin/install_enstore_html
After this step you should be able to access the following web site:
http://www.the_host/enstore/
where the_host is the name of the enstore head node as defined in enstore configuration file. In this particular case it is gccenmvr16a.fnal.gov. Not all web pages are available yet, as they get produced by running enstore servers.

#### Enstore databases
Enstore has 3 databases: file/volume, accounting, and drivestat.
1. enstoredb - file/volume database contains information about all files written to enstore and all volumes (tapes) defined in enstore
2. accounting -contains information about all successful and failed data transfers
3. drivestat database contains information about tape drives configured in the system
There is one more database (operation), which is used only at FNAL. All these databases can be served by separate DB servers or just by one (this is defined in enstore configuration file). Install PosrgresQL on the server(s) defined in the enstore configuration file. The script ($ENSTORE_DIR/sbin/create_database.py), which configures and creates databases uses enstore configuration, but does not consider the host name. The configuration entries for databases are:
file/volume (enstoredb) – database
accounting – accounting_server
drivestat – drivestat_server
operation – no dedicated enstore server

Described here installation procedure is based on the assumption that the installation starts on the node where enstore configuration server will run – enstore head node.
enstoredb
check what node enstoredb will be running on:
[enstore@enmvr026 ~]$ enstore conf --show database
{'db_dir': '/diskb/enstore/enstore-db-backup',
 'db_host': 'enmvr026.fnal.gov',
 'db_port': 8888,
 'dbarea': '/diskb/enstore/enstore-db',
 'dbhost': 'enmvr026.fnal.gov',
 'dbname': 'enstoredb',
 'dbport': 8888,
 'dbserverowner': 'products',
 'dbuser': 'enstore',
 'jou_dir': '/diskb/enstore/enstore-journal',
 'status': ('ok', None)}
According to the output enstoredb will be running on host enmvr026.fnal.gov The following needs to be done as user “root” with enstore environment (which can be done by sourcing ~enstore/site_specific/config/setup-enstore for instance).
Create and start enstoredb:
[root@enmvr026]# python $ENSTORE_DIR/sbin/create_database.py enstoredb

Update DB :
[root@enmvr026]# python $ENSTORE_DIR/sbin/update_database_schema.py enstoredb
2013-08-22 13:53:40 : Executing command downloadXml --dbms=postgres --host=enmvr026.fnal.gov --dbname=enstoredb --port=8888 --user=enstore
diffxml2ddl --dbms=postgres /opt/enstore/databases/schemas/xml/enstoredb.xml schema.xml > enstoredb_diff_tmp.sql
2013-08-22 13:53:40 : successfully created diff DDL file: enstoredb_update.sql
2013-08-22 13:53:40 : examine the content of this file
2013-08-22 13:53:40 : after that apply to database like so:
2013-08-22 13:53:40 : psql -h enmvr026.fnal.gov -p 8888 -U enstore enstoredb -f enstoredb_update.sql
[root@enmvr026]# psql -h enmvr026.fnal.gov -p 8888 -U enstore enstoredb -f enstoredb_update.sql

For accounting, drivestat, operation (just FNAL) repeat steps done for enstoredb, replacing “enstoredb” with “ accounting”, “drivestat”, “operation”.

#### Enstore cron jobs
Install cron jobs defined in enstore configuration file (this must be done on each node in enstore configuration):
[root@enmvr026]# $ENSTORE_DIR/tools/install_crons.py

### Starting, restarting and stopping enstore

As described in “ Configuring Enstore“ Enstore starts automatically on boot on each Enstore machine, but they need to get (re)booted in a certain order:
1. Head node.
2. Rest of servers.
3. Movers.
Enstore can also be started, restarted, or stopped by corresponding enstore command in two different ways (NOTE! You must be user “enstore”!):
1. Locally on each enstore server:
  [enstore@enmvr026 ~]$ enstore start
  Outputs actions (if no output there is nothing to start on this node).
2. Remotely on a selected server, group of servers or the whole set of servers. This command uses farmlets:
  [enstore@gccenmvr16a ~]$ enstore Estart
  This command starts enstore on all nodes in the order, defined in farmlet “enstore”
  [enstore@gccenmvr16a ~]$ enstore Estart servers
  This command starts enstore on all nodes in the order, defined in farmlet “servers”

To check what enstore related processes are running you can use the following commands:
EPS – to see what entsore related processes run locally
enstore EPS - to see what entsore related processes run on all enstore nodes
enstore EPS servers - to see what entsore related processes run on servers defined in farmlet “servers”.